## Slide 1
The Next Generation FVCOM: Algorithms and Progresses
http://fvcom.smast.umassd.edu/
http://www.fvcom.org
Siqi Li, Changsheng Chen, Jianhua Qi, Geoffrey Cowles
University of Massachusetts School of Marine Science
New Bedford, MA 02744

## Slide 2
Outline
A brief review of current FVCOM mode-split and semi-implicit solvers.
The next-generation FVCOM: Hybrid Eulerian-Lagrangian, semi-implicit/implicit time integration. In particular,
The second-order backward difference time integration scheme (BDF2).
The operator-integration-factor splitting (OIFS) algorithm for horizontal advection.
Fully implicit schemes for vertical advection.
Semi-implicit scheme for water elevation.
Update of MPI-OpenMP combined parallelization.

## Slide 3
FVCOM source code
Cartesian/Spherical coordinates
FVCOM
2-D and 3-D Wet/Dry Treatment Methods
Options to Select Multi Radiation Open Boundaries
Forcings:
Tides (equilibrium and from open boundaries)
Winds or wind stresses, air pressure gradients
Net heat flux/shortwave radiation
Precipitation/evaporation
River discharges, groundwaters, and WWTP outfalls
Open boundary fluxes
MPI/OpenMP Parallel
NetCDF Output
Nudging and OI Assimilations
Reduced/Ensemble Kalman Filters (RRKF, EnKF, ETKF, EnSKF, SEIK)
Polar stereographic projecting-spherical coordination nested module at North Polar
EMSF coupler with Multi-domain WRF
One-way and Two-way Nesting based on EMSF
ViSiT monitoring
Existing Model Modules
Existing Technology Modules
Key:
3-D Sediment Models (SEM): Non-cohesive/cohesive
Generalized Biological Model (GBM, ERSEM)
Water Quality Models
(UG-RCA, UG-QUAL-ICM)
Lagrangian Fish Population Models
Surface Wave Models (SWAVE/UNSWAN/WWIII)
Non-hydrostatic Solvers
(Pressure correction/projection)
Ice Models (UG-CICE: Seas and freshwater lakes)
Emerged and/or Submerged Dike-Groyne Modules
Library linking to other models
New Modules
One-way Multi-Model or Domain Nesting
Review of FVCOM
Vegetation Model
General Ocean Turbulence Model (GOTM)
EMSF coupler with WW3 and NWM

## Slide 4
Vertical Coordinates
Generalized terrain-following coordinate transformations based on the approach described in Pietrzak et al. (2002) (Ocean Modeling, 3, 173-205).
Hf
Uniform thicknesses in surface mixing and bottom boundary layers
Avoiding artificial gradient due to precipitation via evaporation
SST/SSS assimilation at the same depth.
s-coordinate
-coordinate
Watershed,
Inter-tidal zone,
Flooded areas,
with a mean
water depth
of ≤ 0
Review of FVCOM
A hybrid coordinate
FVCOM Solvers
Time integration:
1) Mode-splitting and 2) semi-implicit solvers
Mode-splitting:
2-D barotropic mode (ΔTE) and 3-D baroclinic mode (ΔTI), a recommended ratio of ΔTI/ΔTE is 10.
Advantages: Easily set; able to run a 2-D model separately; does not depend on libraries of matrix solvers, etc.
Disadvantage: 2D-3D mode adjustments could cause numerical oscillations in the deep ocean.
Semi-implicit:
FVCOM is solved in a single time step (ΔTI)
Advantage: faster, no adjustment needed, suitable for basin and global applications
Disadvantage: Requires PETSc (scalable sparse matrix solver library).

## Slide 5
Limitation in Applications
Remarks on FVCOM Performances
Merits
Unstructured-grid.
Volume conservations.
Hydrostatic/non-hydrostatic dynamics.
Options for multi-finite-volume advection and time integration schemes.
Simple module structures of the source.
Well-validated via various benchmark test problems through inter-model comparisons with ROMS.
Computationally efficient as finite-difference models.
Coupled fully with ice, sediments, surface waves, vegetation, WRF, and ecosystem/water quality models.
Multiple choices in data assimilation, including nudging, OI, and various Kalman filters.
Successful application to estuaries, coastal to global ocean.
Allows a straight wall in the terrain-following coordinates
Challenging
Both mode-split and semi-implicit integration solver is constrained by the Courant-Friedrichs-Lewy (CFL) condition. In general,
: the internal time step
.
when either mode-splitting or semi-explicit is used.
When applying FVCOM to an estuary with a horizontal resolution of a few meters, the time step is required to be very small, especially in a narrow water passage with strong flow.

## Slide 6
Proposed solutions
Solution 1:
Adjustable based on the magnitude of the velocity.
Advantages:
Simple to be implemented, since the adjustment can be done based on the CFL number constraint.
Ensure numerical stability during unusual extreme storm events.
Disadvantages:
In most cases, the model blows up at a local single cell or node, and the adjustment is made over the entire domain, affecting computational efficiency.
The time step is still constrained by the CFL number.
Solution 2:
Upgrade by implementing an implicit or semi-Lagrangian solver.
Advantages:
The time step is not constrained by the CFL condition or allows a larger CFL number.
Significantly improvement in numerical stability.
Disadvantages:
Enhancing numerical diffusion.
Affecting computational efficiency.
Although the Lagrangian method has no numerical dispersion, the inaccuracy of inverse particle-tracking and interpolation could lead to numerical bias that may be larger than dispersion.

## Slide 7
Proposed solutions
An Illustrative Example of the Eulerian-Lagrangian Method
i,j
i,j+1
i-1,j
i+1,j
i,j-1
i-1,j-1
i-1,j+1
i+1,j-1
i+1,j+1
The diffusion equation for a concentration C is given as
Discretizing using Lagrangian inverse tracking on the left side and Eulerian central difference scheme on the right side, we have
Then, at the ith and jth node can be determined by
The key point is how to determined Two steps:
After using the velocity at the time step (n+1) backward to find P, one can use the interpolation method to determine from surrounding nodes.

## Slide 8
Proposed solutions
Merits:
No advection equations are involved, so it does not have numerical dispersion!
It is numerically stable with a larger CFL number.
Allowing a larger time step in the numerical integration.
Challenging:
Numerical diffusions due to inaccurate Lagrangian particle tracking and interpolation could be significant. Implementing the high-order particle tracking and interpolation methods, like the 4th-order Runge-Katta method or the Discontinuous Galerkin method, could be helpful.
Computational efficiency.
Boundary treatments.
Particle path lines often intersect and/or disperse, making it difficult to resolve the fluid interactions accurately.
Ensuring particle tracking accuracy in sharp gradient areas is crucial, as it can significantly impact the overall simulation results.
Since the horizontal velocity is usually one or two orders of magnitude larger than the vertical velocity, the characteristic trajectories in a 3-D space are at distinct scales of the motion in the horizontal and vertical.

## Slide 9
FVCOM-SWAVE
Explicit
SWAVE
Semi-Lagrangian
The time required
(1 processor)
Schemes | Time (hours)
FVCOM-SWAVE explicit | 0.83
SWAVE-Semi-Lag (60 sec) | 3.0
SWAVE-Semi-Lag (30 sec) | 6.0
SWAVE Semi-Lag (5 sec) | 36
A
B
Site B
Site A
Example: Semi-Lagrangian scheme

## Slide 10
Current versions of FVCOM
The governing equations in the generalized spherical coordinates are given as
where

z
x
y

## Slide 11
()
F
F
F
F
F
F
F
F
F
F
F
F
F:
Cell-centered
Cell vertex median
u,v, T, S
u,v, T, S
r=r2
r=-1
r= 0
0.5
The horizontal
The vertical
Grid: Non-overlapping unstructured-grid
triangles
: at centroids
N: The total centroid number
M: The total node number
On the ith triangle, three nodes are defined as
=1:3; counted clockwise.
On the jth node, the total number of the surrounding triangles connected to this node is defined as , counted by , and
Avoid the errors in forcings due to various triangle sizes
()
()
()
()
()
()
()
()
()
()
()
()
Grid designs

## Slide 12
Current versions of FVCOM
FXADV , FYADV | Zonal and meridional components of advection terms
FXCOR , FYCOR | Zonal and meridional components of the Coriolis terms.
FXCOR , FYCOR | Zonal and meridional components of barotropic pressure gradient terms.
FXSP , FYSP | Zonal and meridional components of barotropic surface pressure forcing terms
FXBCP , FYBCP | Zonal and meridional components of baroclinic pressure gradient forcing terms
FXHVIS , FYHVIS | Zonal and meridional components of horizontal diffusion terms
FXC , FYC | The zonal and meridional components of curvature terms in the spherical coordinates.
To simplify the description of numerical algorithms, we use the hydrostatic momentum equations, for example.
Here,
In the current version of FVCOM, the momentum equations are solved numerically in two steps. In particular,
Step 1: Explicit: the 2nd-order accurate 4th Runge-Katta scheme. Constrained by the CFL condition
Step 2: Implicit: Absolute stable, no constrained by the CFL condition

## Slide 13
The advection terms are calculated by an upwind scheme with a modified Runge-Kutta time-stepping scheme for the 2-D mode and an upwind or a modified Runge-Kutta scheme for the 3-D mode (Kobayashi, 1999).
1. Explicit method
)
, , are determined by a least-square method with velocity values at 4 cell centered points. are location of the triangular central cell.
The x and y components of the horizontal advection are calculated numerically by
: normal velocity on edge, : edge length, Dm is depth
=
=
: cell-centered point of the surrounding triangle,
NBi(m): the neighbor triangle, (): the centered location of the ith triangle.
u,vcos
u,vcos
u,vcos
u,vcos
u,vcos
u,vcos
u,vcos
u,vcos
u,vcos
u,vcos
)
MCT
MCE:The momentum control element, a triangle with at its centroid.
Current versions of FVCOM

## Slide 14
;
)+ )
;
; ;
; ; ;
For example, the surface elevation is determined by the continuity equations given as
The same Runge-Kutta scheme is used for horizontal advection terms in the momentum equations
Numerically integrated using the modified Runge-Kutta time-stepping scheme with a second-order approximation:
TCE: The tracer control element: an area with a node as a center and bounded triangles with at its centroid.

Current versions of FVCOM

## Slide 15
Current versions of FVCOM
Step 2: Vertical diffusion terms:
They are tridiagonal equations, and the solution can be determined without a matrix solver's request.
Vertical discretization

## Slide 16
Tracer equations (temperature, salinity, sediment concentration, etc.). For example, the temperature equation
1. The second-order upwind scheme:
2. Total variational diminishing (TVD) scheme (Dr. O. A. Nøst’s team, Akvaplan-niva, Norway):
Flux limiters:
SUPERBEE: )
)
TCE
T
T
T
T
T
T
T
T
T
T
c
d
f
j is the triangle centroid ID, and i is the index of the central node of .
Determining
is the area determined by the elements with the i node in the upstream region
Current versions of FVCOM

## Slide 17
Next-generation FVCOM
Updating FVCOM with hybrid Eulerian-Operator-Integration-Factor Splitting (OIFS) method as an alternative solver option.
Note: Use the -coordinate equation to explain how this method works. The FVCOM code is modified based on the generalized terrain-followed spherical and Cartesian coordinates
Step 1: Solve the horizontal terms using the 2nd-order backward OIFS method.
Step 2: Solve the vertical diffusion and advection terms implicitly by following the algorithm used in the current version of FVCOM.
Here,
and do not include terms of horizontal advection on terms.
is the Lagrangian time step.
and are the x and y components of the Lagrangian velocity.
Moving the vertical advection to the vertical diffusion equation to avoid the OIFS solvers in two distinct motion scales in the horizontal and vertical.
Determining the Lagrangian velocity at the nth and (n-1)th time steps using the OIFS method can avoid deficiencies in Lagrangian tracking.

## Slide 18
Next-generation FVCOM
Similarities and differences between semi-Lagrangian and OIFS methods
Both solve the conservative advection equations to determine the Lagrangian velocity: and
The semi-Lagrangian method uses forward/backward particle tracking on characteristic lines.
The OIFS method solves the conservative advection equations in the Eulerian space (Maday et al. 1990).
An example to illustrate the similarities of these two methods
Let us consider a one-dimensional case, for example.
For the semi-Lagrangian method, we have:
For OIFS method, we have:
This equation can be obtained using the Taylor expansion from the above semi-Lagrangain equation , i.e.

## Slide 19
Next-generation FVCOM
The semi-Lagrangian Method | The OIFS Method
Becomes increasingly more cost-effective with increasing time-step. On a distributed-memory computer, the departure point of a specific grid point may lie off-processor. The online 2nd-order accurate 4th-order Runge-Katta particle tracking program in FVCOM can be directly used for the forward/backward tracking to determine the departure point. However, particle tracking requires the treatment of various open and solid boundaries, which can increase numerical uncertainty around boundaries. An interpolation stencil, which is a set of points used to perform the interpolation, must be coded in the grid. The interpolation accuracy depends on the interpolation scheme, with high-order interpolation functions being preferred for their accuracy. | The success of the method relies on solving an advection problem efficiently. Multi-advection operators can be implemented. OIFS can take advantage of unstructured grids in the current versions of FVCOM. The MPI/OpenMP parallelization methods, which are seamlessly integrated into the current version of FVCOM, can be directly applied to the OIFS method, ensuring compatibility and ease of use. The departure point values do not rely on interpolation, as in the semi-Lagrangian method, which could avoid the numerical errors caused by interpolation. OIFS can be one option for FVCOM solvers without changing the grid setup.
Advantages and Challenging of Implementing semi-Lagrangian and OIFS Methods into FVCOM

## Slide 20
Next-generation FVCOM
The approaches used for Step 1
Determining the backward Lagrangian velocities at the nth and (n-1)th time steps by solving the two-dimensional advection equation within the time interval of :
Note: One can solve these two equations using the same 2nd-order Runge-Katta explicit method from the current version of FVCOM with a sub-time step within the time interval of or implementing an implicit Runge-Katta method.

## Slide 21
Next-generation FVCOM
1. Explicit solver with a sub-time step within the time interval of
The current version of FVC OM has a 2nd KR integration method to solve the horizontal advection terms. The difference here is that we only solve the horizontal advection equations over the time interval of . One can easily use the same explicit 2nd KR method to solve the conservative advection equations.
According to the momentum conservation, the Lagrangian velocity at nth and (n-1)th time steps equals
And
This approach can increase the maximum CFL number.

## Slide 22
Next-generation FVCOM
2. Implicit solver with a sub-time step within the time interval of
Solving the advection equation using the tracer control element using the combined implicit TVD (spatial) and RK (time integration) algorithms (Note: This helps reduce the matrix size for the implicit solver).
For momentum equation,
Step 1: interpolate the velocity from individual triangular centroids to the triangle’s nodes.
): the total number of the surrounding triangle with a connection to the jth node.
Step 2: Construct the matrix based on the finite-volume control element centered at the tringle’s nodes.
is the normal velocity calculated by interpolation or extrapolation between the time interval n-1 and n.
Introducing the second-order accuracy of the total variational diminishing (TVD) method to construct the matrix for and .
Flux limiters

## Slide 23
Vertical diffusion and advection equations:
They are tridiagonal equations, and the solution can be determined without a matrix solver's request.
Next-generation FVCOM

## Slide 24
Next-generation FVCOM
Updates of the code modifications
Team members | Contributions
Dr. S. Li | Leading the development of implementing the OIFS methods: the code modification and benchmark tests.
Dr. C. Chen | Supervising the developments in numerical schemes and code structures.
Dr. J. Qi | Modifying the implicit solver of the diffusion-advection equation: the code modification and benchmark tests.
Dr. G. Cowles | Supervising the new code parallelization.
Team members and their contributions
Time | Completions or ongoing tasks
March-April 2024 | Completed numerical algorithm designs in Mathematics.
May-June 2024 | Completed the code modification to include the vertical advection in the implicit solver and conducted an initial benchmark test by comparing it with the current version of FVCOM.
May-June 2024 | Completed the code development of the implicit OIFS method.
July-August 2024 | Test the implicit OIFS method on a benchmark test problem and evaluate the code by comparing the results with the current version of FVCOM. Continue to debug the implicit diffusion-advection solvers for benchmark test problems.

## Slide 25
Next-generation FVCOM
Example: Comparisons between the implicit vertical diffusion-advection solver and upwind and TVD/MPDATA solvers.
Upwind scheme
TVD/MPDATA scheme
Implicit vertical advection scheme
Temperature
Salinity

## Slide 26
Next-generation FVCOM
Example: Comparisons between the implicit vertical diffusion-advection solver and upwind and TVD/MPDAT solvers.

## Slide 27: OpenMP for FVCOM-SWAN model
Update of MPI/Open MP code debugging
Subroutine | Wall time | Wall time |  |  |  | 
 | Threads: 1 Task(s): 1 | Threads: 1 Task(s): 1 | Threads: 2 Task(s): 1 | Threads: 4 Task(s): 1 | Threads: 1 Task(s): 2 | Threads: 1 Task(s): 4
SWOMPU1 | 0.1179 | 0.1179 | 0.0778 | 0.0437 | 0.0598 | 0.0314
ADV_N | 0.1008 | 0.1008 | 0.0555 | 0.0322 | 0.0694 | 0.0482
SWOMPU2 | 0.2073 | 0.2073 | 0.1636 | 0.1636 | 0.1055 | 0.0552
Total |  |  |  |  |  | 
SWCOMP |  | 0.4524 | 0.3250 | 0.2669 | 0.2770 | 0.1695
internal_step |  | 0.5291 | 0.3901 | 0.3259 | 0.3171 | 0.1928
Initial
FVCOM
modules
SWAVE
module
Time End?
Yes
No
Finish
OpenMP starts
OpenMP finishes
Implementation was initially done for one OpenMP parallel block in the SWAVE subroutines to reduce the start-up time of OpenMP threads
The hotspots of the FVCOM-SWAVE model are the subroutines in the SWAVE module.
Updated from Dr. J. K. Chen
Time-consuming statistics in each step of the FVCOM-SWAN model with OpenMP

## Slide 28
The new OIFS solvers, which are being implemented in FVCOM, will expand FVCOM’s capability of solving the problem with a meter-order resolution with a large CFL number or no CFL constraints.
The next-generation FVCOM is designed to cater to a wide range of user needs. It will provide users with various multi-solvers, including RK-upwind, TVD/MPDATA, and OIFS. The inter-solver comparisons could help the solver’s selection with the required accuracy.
The combined MPI/OpenMP parallelization could significantly improve the FVCOM’s computational efficiency.
Summary